## Slide 1: STC42A Hydrogen Sensor
Automotive Compliant (AEC-Q100 Grade 2)

## Slide 2
USA
FMVSS 305a
CN
GB 38031-2025
World
GTR20 Phase2
Thermal Runaway & Propagation
Overcharge / Short circuit
Physical Damage
Overheating
TR Propagation
Comply with Regulations: Warn 5 Minutes before Harm
Thermal Runaway
Heat of neighboring cell
Conductive heat transfer
Heat from flame

## Slide 3: STC42A Specifications
© Copyright Sensirion, Switzerland
3
Optimized Hydrogen Gas Sensing for Thermal Runaway Applications
H2 range: 0 – 40vol%
Accuracy: ± (0.4vol% + 2% of reading)
Typical response time: 1s (τ63)
Supply voltage: 3.3V, 5V DC
Operation:
0.1…60s sampling interval (cont.)
On-demand (single shot)
3mm
3.5mm
1mm
Automotive compliant: AEC-Q100 grade 2 2)
1) Continuous measurement mode at 1Hz - and <7µA in low-power mode at 0.03Hz.
2) Qualification standard developed by the Automotive Electronics Council (AEC) that defines stress tests and reliability requirements for integrated circuits used in automotive applications.
Avg current consumption: <0.7mA 1)

## Slide 4: Key Advantages of the STC42A Sensor
Individual sensor calibration and on chip compensation
Excellent and proven long-term stability
Engineered and manufactured in Switzerland
Robustness to shock and vibration
SMD soldering
Digital I2C interface for communication and
automatic AH compensation
PFAS-free membrane
STC42A Hydrogen Sensor combines advanced sensing performance with automotive‑grade robustness
Low power mode via interrupt pin

## Slide 5
Notes: At Sensirion, we look forward to collaborating closely with our channel partners to identify and unlock new opportunities for the STC42A, driving innovation in the rapidly expanding hydrogen‑sensing market.